## Slide 1: WiE WSF TSC WL Performance DSA-SPDK-Accel_Perf -Storage
Li Longtan - xPSD
Apr 22, 2022

## Slide 2
Agenda
Workload Introduction & Architecture
Test Cases & Configurations
Performance result & analysis
  DSA HW memory copy
  SW memory copy
  DSA HW memory copy with SNC4 disabled
Conclusion and Next Step
2

## Slide 3
What is DSA
  Data Streaming Accelerator
    Device providing high-performance data copy and transformation accelerator targeted for optimizing streaming data movement and transformation operations.
    Bandwidth ~30 GB/s throughput.
Workloads/Usages
    Storage
    Networking
    PCIe NTB
Workload Introduction
3

## Slide 4: Abstracted Internal Block Diagram of DSA
Device basic components
  Work Queues(WQ)
    Share Work Queue
    Dedicated Work Queue
  Engines
Descriptor
    Batch Descriptor(bd)
    Work Descriptor(wd)
5

## Slide 5
SPDK Accelerator
  The Storage Performance Development Kit (SPDK) provides a set of tools and libraries for writing high performance, scalable, user-mode storage applications.
  SPDK provides a framework for abstracting general acceleration capabilities
    hardware acceleration engines such as the Intel(R) I/O Acceleration Technology (IOAT) engine and the Intel(R) Data Streaming Accelerator (DSA) engine.
    software plug-in module
Workload Introduction
5

## Slide 6
Intel SPR
HW
SW
OS: Ubuntu 18.04
OS
Architecture - SW Stack
6
SPDK 22.01
container
DPDK 21.11
accel_perf

## Slide 7
Test Case
7
Test case
  copy
  crc32c
  fill
  compare
  dualcast
  copy_crc32c

## Slide 8: BIOS and Boot Setting
8
BIOS setting | Required setting
Hyper-Threading | DISABLE
CPU power and performance policy | Performance
SpeedStep (P) | ENABLE
turbo boost technology | ENABLE
processor C6 | DISABLE
C1E | DISABLE
Package C State | C0/C1 state
Hardware P-States | DISABLE
Intel VT for directed I/O | ENABLE
Boot setting | BOOT_IMAGE=(hd0,gpt2)/vmlinuz-5.15.0-spr.bkc.pc.2.10.0.x86_64 root=/dev/mapper/cs_r028s002_zp31l10c01-root ro crashkernel=auto resume=/dev/mapper/cs_r028s002_zp31l10c01-swap rd.lvm.lv=cs_r028s002_zp31l10c01/root rd.lvm.lv=cs_r028s002_zp31l10c01/swap rhgb quiet intel_iommu=on iommu=pt hugepagesz=2M hugepages=512

## Slide 9: System Configuration
9
Name | Rasp-3470
Time | Wed Apr 13 16:02:24 UTC 2022
Manufacturer | Intel Corporation
Product Name | ArcherCity
BIOS Version | EGSDCRB1.86B.0073.D14.2201260628
OS | CentOS Stream 8
Kernel | 5.15.0-spr.bkc.pc.2.10.0.x86_64
Microcode | 0x8e0001c0
IRQ Balance | Enabled
CPU Model | Genuine Intel(R) CPU 0000%@1.8GHz (E0 Q0A9)
Base Frequency | 1.8GHz
Maximum Frequency | 3.5GHz
All-core Maximum Frequency | 2.8GHz
CPU(s) | 96
Thread(s) per Core | 1
Core(s) per Socket | 48
Socket(s) | 2
NUMA Node(s) | 8
Prefetchers | L2 HW, L2 Adj., DCU HW, DCU IP
Turbo | Enabled
PPIN(s) | 147f440857df30dd,147f4a08c9d9c124
Power & Perf Policy | Performance
TDP | 350 watts
Frequency Driver | intel_pstate
Frequency Governer | performance
Frequency (MHz) | 3500
Max C-State | 9
Installed Memory | 512GB (32x16GB DDR5 4800MT/s [4400MT/s])
Huge Pages Size | 2048 kB
Transparent Huge Pages | always
Automatic NUMA Balancing | Enabled
NIC Summary | 1x Ethernet Controller I225-LM
Drive Summary | 1x 1T INTELSSDSC2KB96, 2x 2T SAMSUNG MZPLJ1T6HBJR-00007

## Slide 10: Performance Analysis – DSA HW memory Copy
CPU utilization : 100%, working frequency : 3.5 GHz
One DSA device Bandwidth 30GB/s
10
SPDK DSA copy bandwidth(MB/s) |  |  |  |  |  |  |  |  |  |  |  |  | 
size | 1c-1t-1q | 2c-1t-1q | 2c-4t-1q | 2c-4t-16q | 2c-4t-32q | 4c-1t-1q | 4c-4t-1q | 4c-4t-16q | 4c-4t-32q | 8c-1t-1q | 8c-4t-1q | 8c-4t-16q | 8c-4t-32q
4K | 4,075 | 8,241 | 26,955 | 56,787 | 56,921 | 16,550 | 57,359 | 113,591 | 112,740 | 33,000 | 97,511 | 113,109 | 112,941
16K | 11,400 | 23,213 | 58,636 | 57,799 | 59,759 | 45,590 | 117,241 | 119,169 | 116,941 | 81,704 | 118,816 | 117,823 | 119,168
32K | 16,781 | 32,936 | 60,155 | 60,231 | 60,321 | 65,686 | 120,332 | 119,943 | 120,368 | 113,627 | 120,425 | 120,514 | 120,566
64K | 21,130 | 42,843 | 60,597 | 59,340 | 60,567 | 83,940 | 121,202 | 120,253 | 121,158 | 120,650 | 120,900 | 121,148 | 120,208
Chart: SPDK DSA copy Performance
| 1c1t1q | 2c1t1q | 2c4t1q | 2c4t16q | 2c4t32q | 4c1t1q | 4c4t1q | 4c4t16q | 4c4t32q | 8c1t1q | 8c4t1q | 8c4t16q | 8c4t32q
4k | 4075 | 8241 | 26955 | 56787 | 56921 | 16550 | 57359 | 113591 | 112740 | 33000 | 97511 | 113109 | 112941
16k | 11400 | 23213 | 58636 | 57799 | 59759 | 45590 | 117241 | 119169 | 116941 | 81704 | 118816 | 117823 | 119168
32k | 16781 | 32936 | 60155 | 60231 | 60321 | 65686 | 120332 | 119943 | 120368 | 113627 | 120425 | 120514 | 120566
64k | 21130 | 42843 | 60597 | 59340 | 60567 | 83940 | 121202 | 120253 | 121158 | 120650 | 120900 | 121148 | 120208

## Slide 11: Call stack Analysis – DSA HW memory Copy
11
module | 1c1t1q,4k | 1c1t1q,16k | 1c1t1q,32k | 1c1t1q,64k | 8c1t1q,4k | 8c1t1q, 16k | 8c1t1q, 32k | 8c1t1q, 64k
accel_perf(%) | 80.92 | 92.57 | 92.32 | 92.07 | 98.77 | 98.74 | 98.77 | 98.68
Performance(MB/s) | 4,075 | 11,400 | 16,781 | 21,130 | 33,000 | 81,704 | 11,3627 | 12,0650
SPDK DSA copy core usage(%) |  |  |  |  |  |  |  |  | 
module | Symbol in | 1c1t1q,4k | 1c1t1q,16k | 1c1t1q,32k | 1c1t1q,64k | 8c1t1q,4k | 8c1t1q, 16k | 8c1t1q, 32k | 8c1t1q, 64k
accel-perf | thread_poll | 24.84 | 30.41 | 31.61 | 32.22 | 36.65 | 39.16 | 39.89 | 41.41
 | spdk_idxd_process_events | 12.82 | 10.43 | 8.87 | 7.55 | 16.99 | 13.85 | 11.81 | 9.98
 | spdk_thread_poll | 9.07 | 10.92 | 10.83 | 11.56 | 8.33 | 9.06 | 9.54 | 9.97
Accel-perf | reactor_post_process_lw_thread | 5.05 | 5.69 | 5.91 | 6.18 | 4.62 | 4.93 | 5.24 | 5.40
 | reactor_run | 4.77 | 5.93 | 6.09 | 6.30 | 5.88 | 6.42 | 6.82 | 6.16
spdk_idxd_process_event function check DSA IO completion status

## Slide 12: Performance Analysis – SW memory Copy
SPDK software copy bandwidth(MB/s) |  |  |  |  |  | 
size | 1c-1t-1q | 8c-1t-1q | 8c-4t-1q | 8c-4t-16q | 8c-4t-32q | 8c-4t-64q
4K | 63,414 | 631,434 | 379,399 | 302,235 | 299,004 | 198,184
16K | 136,855 | 470,411 | 334,364 | 295,965 | 130,546 | 130,986
32K | 42,169 | 338,938 | 335,344 | 131,267 | 131,449 | 104,259
64K | 44,218 | 353,836 | 351,864 | 132,413 | 106,094 | 71,243
CPU utilization : 100%, working frequency : 3.5 GHz
12
Chart: SPDK sw copy performance
| 1c1t1q | 8c1t1q | 8c4t1q | 8c4t16q | 8c4t32q | 8c4t64q
4K | 63414 | 631434 | 379399 | 302235 | 299004 | 198184
16K | 136855 | 470411 | 334364 | 295965 | 130546 | 130986
32K | 42169 | 338938 | 335344 | 131267 | 131449 | 104259
64k | 44218 | 353836 | 351864 | 132413 | 106094 | 71243

## Slide 13: Call Stack Analysis – SW memory Copy
13
module | 1c1t1p,4k | 1c1t1p,16k | 1c1t1p,32k | 1c1t1p,64k | 8c1t1q,4k | 8c1t1q,16k | 8c1t1q, 32k | 8c1t1q, 64k
libc-2.28.so | 53.06 | 79.67 | 81.96 | 83.89 | 64.29 | 64.54 | 64.37 | 84.66
accel_perf | 38.55 | 11.87 | 9.12 | 8.31 | 34.46 | 34.17 | 34.31 | 14.08
kernel | 4.28 | 4.24 | 4.29 | 3.97 | 0.71 | 0.73 | 0.74 | 0.72
Performance(MB/s) | 63,414 | 136,855 | 42,169 | 44,218 | 631,434 | 470,411 | 338,938 | 353,836
SPDK Software copy core usage(%) |  |  |  |  |  |  |  |  | 
module | Symbol in | 1c1t1p 4k | 1c1t1p,16k | 1c1t1p,32k | 1c1t1p,64k | 8c1t1q,4k | 8c1t1q, 16k | 8c1t1q, 32k | 8c1t1q, 64k
libc-2.28.so | __memcmp_avx2_movbe | 36.45 | 53.36 | 49.62 | 0 | 44.65 | 44.24 | 44.77 | 0
 | __memmove_avx_unaligned_erms | 16.53 | 26.25 | 32.28 | 83.83 | 19.62 | 20.29 | 19.59 | 84.65
accel-perf | thread_poll | 9.38 | 3.15 | 2.19 | 1.73 | 8.19 | 8.09 | 7.99 | 2.48
 | spdk_thread_poll | 4.37 | 1.52 | 0.89 | 0.75 | 3.16 | 3.05 | 3.15 | 1.15
Accel-perf | reactor_post_process_lw_thread | 2.44 | 0.75 | 0.34 | 0.31 | 1.87 | 1.85 | 1.83 | 0.69
 | reactor_run | 2.42 | 0.66 | 0.80 | 0.87 | 1.96 | 1.96 | 1.97 | 0.99
SW copy use memcmp/memmove instructions which have CPU utilization almost at 70~85%, while DSA technology offload the operation into DSA HW device with the cost of read/write device.
Notes: Using perf tool capture the function core usage

## Slide 14
Performance Results​
The offloading of copy&crc32c to DSA device can reduce CPU utilization largely.
DSA Copy&CRC32 can achieve 120GB/s bandwidth with 4 DSA devices in one socket.
Next Step​
  Using Perf tool to monitor DSA device utilization
  Analyze Other DSA functions
14
Conclusion & Next Step

## Slide 15: Photo Example On Lower Half
Thank You
15

## Slide 16
Backup
16

## Slide 17: Performance Analysis – DSA CRC32c
SPDK DSA CRC32c bandwidth(MB/s) |  |  |  |  |  |  |  |  |  |  |  |  |  | 
size | 1c-1t-1q | 2c-1t-1q | 2c-4t-1q | 2c-4t-16q | 2c-4t-32q | 4c-1t-1q | 4c-4t-1q | 4c-4t-16q | 4c-4t-32q | 8c-1t-1q | 8c-4t-1q | 8c-4t-16q | 8c-4t-32q | 8c-4t-64q
4K | 4,367 | 8,054 | 29,322 | 59,777 | 59,885 | 16,194 | 62,270 | 119,568 | 119,775 | 32,885 | 108,011 | 119,312 | 119,649 | 119,752
16K | 12,090 | 22,680 | 60,678 | 60,655 | 60,608 | 45,595 | 121,370 | 121,378 | 121,441 | 95,566 | 121,221 | 121,295 | 121,191 | 121,436
32K | 16,582 | 32,397 | 60,874 | 60,800 | 60,860 | 65,560 | 121,771 | 121,632 | 121,672 | 121,470 | 121,605 | 121,652 | 121,717 | 121,684
64K | 22,190 | 42,692 | 60,953 | 60,882 | 60,939 | 85,502 | 121,917 | 121,777 | 121,713 | 121,842 | 121,752 | 121,835 | 121,909 | 121,917
17
CPU utilization : 100%, working frequency : 3.5 GHz
One DSA device Bandwidth 30GB/s
Chart: SPDK DSA crc32c Performance
| 1c1t1q | 2c1t1q | 2c4t1q | 2c4t16q | 2c4t32q | 4c1t1q | 4c4t1q | 4c4t16q | 4c4t32q | 8c1t1q | 8c4t1q | 8c4t16q | 8c4t32q | 8c4t64q
4K | 4367 | 8054 | 29322 | 59777 | 59885 | 16194 | 62270 | 119568 | 119775 | 32885 | 108011 | 119312 | 119649 | 119752
16K | 12090 | 22680 | 60678 | 60655 | 60705 | 45595 | 121370 | 121378 | 121441 | 95566 | 121221 | 121295 | 121191 | 121436
32K | 16582 | 32397 | 60874 | 60800 | 60831 | 65560 | 121771 | 121632 | 121672 | 121470 | 121605 | 121652 | 121717 | 121684
64K | 22190 | 42725 | 60953 | 60882 | 60901 | 85502 | 121917 | 121777 | 121713 | 121842 | 121752 | 121835 | 121909 | 121917

## Slide 18: Call stack Analysis - DSA CRC32c
18
Shared Object | 1c1t1q,4k | 1c1t1q,16k | 1c1t1q,32k | 1c1t1q,64k | 8c1t1q,4k | 8c1t1q, 16k | 8c1t1q, 32k | 8c1t1q, 64k
accel_perf(%) | 91.22% | 92.10 | 92.36 | 91.87 | 98.70 | 98.68 | 98.76 | 98.72
kernel(%) | 4.34 | 3.91 | 3.80 | 4.04 | 0.73 | 0.75 | 0.73 | 0.75
Performance | 4,367 | 12,090 | 16,582 | 22,190 | 32,885 | 95,566 | 121,470 | 121,842
SPDK DSA crc32c core usage(%) |  |  |  |  |  |  |  |  | 
Shared Object | Symbol in | 1c1t1q,4k | 1c1t1q,16k | 1c1t1q,32k | 1c1t1q,64k | 8c1t1q,4k | 8c1t1q, 16k | 8c1t1q, 32k | 8c1t1q, 64k
accel-perf | thread_poll | 29.01 | 30.18 | 32.04 | 32.17 | 36.24 | 39.36 | 40.18 | 40.73
 | spdk_idxd_process_events | 13.02 | 10.97 | 8.94 | 7.03 | 16.61 | 13.77 | 12.23 | 10.62
 | spdk_thread_poll | 10.66 | 11.16 | 11.41 | 11.59 | 8.32 | 8.94 | 9.22 | 9.80
Accel-perf | reactor_post_process_lw_thread | 5.57 | 5.64 | 6.01 | 6.21 | 6.02 | 5.65 | 5.03 | 5.08
 | reactor_run | 5.31 | 5.84 | 6.02 | 6.08 | 5.83 | 6.25 | 6.51 | 6.81

## Slide 19: Performance Analysis – ISAL CRC32c
CPU utilization : 100%, working frequency : 3.5 GHz
19
Chart: SPDK ISAL crc32c Performance
| 1c1t1q | 8c1t1q | 8c4t1q | 8c4t16q | 8c4t32q | 8c4t64q
4K | 46331 | 481979 | 453244 | 596742 | 614229 | 622754
16K | 76376 | 673707 | 601008 | 726496 | 554199 | 273515
32K | 85945 | 715361 | 667725 | 635748 | 280413 | 279708
64K | 89943 | 728726 | 716717 | 281827 | 282197 | 200092
SPDK ISAL crc32c bandwidth(MB/s) |  |  |  |  |  | 
size | 1c-1t-1q | 8c-1t-1q | 8c-4t-1q | 8c-4t-16q | 8c-4t-32q | 8c-4t-64q
4K | 46,331 | 481,979 | 453,244 | 596,742 | 614,229 | 622,754
16K | 76,376 | 673,707 | 601,008 | 726,496 | 554,199 | 273,515
32K | 85,945 | 715,361 | 667,725 | 635,748 | 280,413 | 279,708
64K | 89,943 | 728,726 | 716,717 | 281,827 | 282,197 | 200,092

## Slide 20: Call stack Analysis - SW CRC32c
20
Shared Object | 1c1t1q,4k | 1c1t1q,16k | 1c1t1q,32k | 1c1t1q,64k | 8c1t1q,4k | 8c1t1q, 16k | 8c1t1q, 32k | 8c1t1q, 64k
accel_perf(%) | 91.96 | 91.57 | 91.75 | 91.87 | 91.88 | 98.64 | 98.73 | 98.72
kernel | 4.06 | 4.27 | 4.12 | 4.04 | 4.01 | 0.75 | 0.72 | 0.73
Performance(MB/s) | 46,331 | 76,376 | 85,945 | 89,943 | 481,979 | 673,707 | 715,361 | 728,726
SPDK SW crc32c core usage(%) |  |  |  |  |  |  |  |  | 
Shared Object | Symbol in | 1c1t1q,4k | 1c1t1q,16k | 1c1t1q,32k | 1c1t1q,64k | 8c1t1q,4k | 8c1t1q, 16k | 8c1t1q, 32k | 8c1t1q, 64k
accel-perf | crc32_iscsi_by16_10.fold_256_B_loop | 40.92 | 70.58 | 80.24 | 82.65 | 50.36 | 81.75 | 89.48 | 89.46
Accel-perf | thread_poll | 8.63 | 3.62 | 2.02 | 0.61 | 4.45 | 1.63 | 0.89 | 0.93
 | spdk_thread_poll | 4.47 | 1.87 | 0.96 | 0.59 | 3.33 | 1.2 | 0.65 | 0.67
 | reactor_post_process_lw_thread | 2.72 | 1.05 | 0.57 | 0.28 | 2.26 | 1.52 | 0.42 | 0.43
Accel-perf | reactor_run | 2.33 | 1.00 | 0.53 | 0.31 | 2.28 | 0.81 | 0.46 | 0.43
SW crc32c has CPU utilization almost at 50~90%, while DSA technology offload the operation into DSA HW device with the cost of read/write device.

## Slide 21: Analysis – Copy Performance Without SNC4
CV
item | 4K |  | CV |  | 16K |  | CV |  | 32K |  | CV |  | 64K |  | CV
1c1q1t | 3545 |  |  |  | 11389 |  |  |  | 15209 |  |  |  | 20430 |  | 
 | 3535 |  |  |  | 11446 |  |  |  | 15651 |  |  |  | 20626 |  | 
 | 3977 | 3739 |  |  | 11247 | 11183.6 |  |  | 16351 | 15847.6 |  |  | 20814 | 20784.4 | 
 | 3562 | 236.978 | 6% |  | 10817 | 235.181 | 2% |  | 16093 | 391.806 | 2% |  | 21076 | 233.798 | 1%
 | 4076 | 3562 |  |  | 11019 | 11247 |  |  | 15934 | 15934 |  |  | 20976 | 20814 | 
8c1q1t | 27684 |  |  |  | 79455 |  |  |  | 108974 |  |  |  | 120658 |  | 
 | 31936 |  |  |  | 76307 |  |  |  | 109640 |  |  |  | 120649 |  | 
 | 30931 | 29236.8 |  |  | 76849 | 76785.6 |  |  | 111124 | 109740 |  |  | 120662 | 120653 | 
 | 27399 | 1841.21 | 6% |  | 76088 | 1433.07 | 2% |  | 108729 | 869.409 | 1% |  | 120645 | 6.3435 | 0%
 | 28234 | 28234 |  |  | 75229 | 76307 |  |  | 110235 | 109640 |  |  | 120649 | 120649 | 
8c1q4t | 67128 |  |  |  | 67119 |  |  |  | 71581 |  |  |  | 118139 |  | 
 | 36746 |  |  |  | 95312 |  |  |  | 119391 |  |  |  | 68453 |  | 
 | 40001 | 50486.2 |  |  | 118826 | 84281.2 |  |  | 119370 | 94308 |  |  | 117964 | 89566.6 | 
 | 53924 | 10997.2 | 22% |  | 70950 | 20073.6 | 24% |  | 72976 | 21287.9 | 23% |  | 68296 | 23382.7 | 26%
 | 54632 | 53924 |  |  | 69199 | 70950 |  |  | 88222 | 88222 |  |  | 74981 | 74981 | 

## Slide 22: Analysis – CRC32c Performance Without SNC4
DSA device Bandwidth performance isn’t stable
AR