## Slide 1
WiE SF TSC WL Performance MLC – Micro benchmark
Chunhua Sun
xPSD – Workload Integration and Enabling (WiE) team
June 2nd, 2022

## Slide 2: Notices & Disclaimers
These are results of internal measurement campaigns and are NOT official claims. This material shall not be used externally.
Results have been estimated or simulated.
Performance varies by use, configuration and other factors. Learn more at www.Intel.com/PerformanceIndex .
Performance results are based on testing as of dates shown in configurations and may not reflect all publicly available updates. See backup for configuration details. No product or component can be absolutely secure.
Your costs and results may vary.
2

## Slide 3: Agenda
WL Introduction
WL SW Stack
KPI Definition
System configuration
Performance Data
  Latency
  Bandwidth
  Core Scaling
Conclusion and Next Step
3

## Slide 4: WL Introduction
MLC: Intel® Memory Latency Checker (Intel® MLC)
Support latest version v3.9a.
KPI: Latency and Bandwidth
An important factor in determining application performance is the Latency required for the application to fetch data from the processor’s cache hierarchy and from the memory subsystem. Besides latency, bandwidth (b/w) also plays a big role in determining performance. So, measuring these latencies and b/w is important to establish a baseline for the system under test, and for performance analysis.
Features:
Measure cache latencies and b/w
Measure cache-to-cache data transfer latencies
Measure latencies for requests addressed to a specific memory controller from a specific core
Measure b/w from a subset of the cores/sockets
Measure b/w for different read/write ratios
4

## Slide 5: WL SW Stack
Backend
Host OS
CentOS/Ubuntu
Intel SPR/ICX
hardware
Cumulus
K8S
Docker
Local
Single node
Local cluster
Node 1
WL Container
WL Container
Node n
WL Container
MLC
Public Cloud
WL Container
WL Container
Cloud Node 1
Cloud Node n
MLC
MLC
MLC 3.9a
Rockylinux 8.5
run_mlc.sh
MLC docker image
5

## Slide 6
6
Initialize memory buffer in target area
Create Latency thread on working core :
issued one load of data, get feedback
Latency = T/N
Latency
KPI Definition
create dummy thread in each socket’s
first core to keep CPU active
.
1.
2.
0.
1. Repeat loading data during specific time T
2. count the repeat times N
Only one working core is used in loading data.
The buffer size is used to determine the measuring of L1/L2/L3/DRAM
buffer size vs cache size
buffer size < L1D cache size，hit in L1, get L1 latency.
L1D cache size < buffer size < L2 cache size, hit in L2 , get L2 latency
L2 cache size < buffer size < L3 cache size, hit in L3 , get L3 latency
buffer size > L3 cache size，miss in L3, get memory latency.
buffer
LLC

## Slide 7: KPI Definition
7
Initialize Read
memory buffer
Create bandwidth thread:
issued to load data
from Read buffer
1. Repeat loading data during specific time T
2. count the repeat times N
Read bandwidth = (Read_buffer_size * N) / T
Bandwidth
Get system’s total bandwidth by adding all working cores’ bandwidth together
(Working core list can be configured in the test.)
The buffer size is used to determine the measuring of L1/L2/L3/DRAM.
Support generating different traffic patterns for different R/W ratio.
1.
1.
2.
Read buffer
Write buffer
LLC
Core Memory Controller DDR
Store
Read For Ownership + Write
Core Memory Controller DDR
Load
Read
Load
Notes: Read : Write = 3 : 1 from memory controller’s view means Read : Write = 2 : 1 from applications’ point of view. Since store instruction = 1 Read(read ownership) + 1 Write
metric_memory bandwidth read (MB/sec)
146,464.3075
metric_memory bandwidth write (MB/sec)
48,873.9343
(Memory controller view) Read/Write Ratio
3/1

## Slide 8: System Configuration
8
System Info | spr97623 | rasp-1519
BIOS Version | EGSDCRB1.86B.0073.D14.2201260628 | WLYDCRB1.SYS.0027.P56.2112200409
OS | CentOS Stream 8 | Red Hat Enterprise Linux 8.2 (Ootpa)
Kernel | 5.15.0-spr.bkc.pc.2.10.0.x86_64 | 4.18.0-305.19.1.el8_4.x86_64
Microcode | 0x8e0001c0 | 0xd000332
Base Frequency | 1.6GHz | 2.6GHz
Maximum Frequency | 3.5GHz | 3.7GHz
All-core Maximum Frequency | 2.6GHz | 3.3GHz
CPU(s) | 240 | 152
Thread(s) per Core | 2 | 2
Core(s) per Socket | 60 | 38
Socket(s) | 2 | 2
NUMA Node(s) | 2 | 2
NUMA cpulist | 0-59,120-179 :: 60-119,180-239 | 0-37,76-113 :: 38-75,114-151
L1d Cache | 48K | 48K
L1i Cache | 32K | 32K
L2 Cache | 2048K | 1280K
L3 Cache | 115200K | 58368K
Prefetchers | DCU HW, DCU IP, L2 HW, L2 Adj. | DCU HW, DCU IP, L2 HW, L2 Adj.
Intel Turbo Boost | Enabled | Enabled
QPI Link | 4 | 3
Memory Installed | 512GB (16x32GB DDR5 4800MT/s ) | 512GB (16x32GB DDR4 2933MT/s )
Power & Perf Policy | Performance | Performance
Automatic NUMA Balancing | Disabled | Disabled

## Slide 9: Latency Measurement
9
L1 Cache
L2 Cache
L3 Cache
DRAM
NUMA0
L3 Latency
UPI
UPI
Core 0
Core n
L1 Latency
L2 Latency
Latency measurement
L1 Latency: ./mlc --idle_latency -e -r -b24K -H
L2 Latency: ./mlc --idle_latency -e -r -b800K -H
L3 Latency (SNC4) : ./mlc --idle_latency -e -r -b6m -H
L3 Latency (SNC1)
Local Memory Latency (SNC4)
Local Memory Latency (SNC1)
Remote Memory Latency (SNC1)
L1 Cache
L2 Cache
SNC1
SNC3
SNC2
SNC0
MC1
MC0
MC2
MC3
Local Memory Latency (SNC4)
SPR(SNC4)
L1 Cache
L2 Cache
L3 Cache
DRAM
NUMA1
Core 0
Core n
L1 Cache
L2 Cache
Remote
Memory Latency
SNC5
SNC7
SNC6
SNC4
MC5
MC4
MC6
MC7
ICX/SPR (SNC1)
UPI
UPI
socket 0
socket 0
socket 1
socket 1
L3 Cache
L3 Latency (SNC4)
Local Memory Latency

## Slide 10: Latency Data Comparison
10
10
Platform | Op-Freq | Uncore Freq | Base-Freq | CPU utilization (1t1c)
ICX1519 | 3.656 GHz | 2.200 GHz | 2.6GHz | 47.390%
SPR97263 | 3.403 GHz | 2.501 GHz | 1.6GHz | 47.295%
Latency(ns) | ICX1519 | SPR97263 | Ref: ICX Target | Ref: SPR Target
L3(SNC4) | / | 26.0 | / | 22.2
L3(SNC1) | 25.4 | 38.0 | 18.1 | 37.0
Local Memory(SNC4) | / | 91.3 | / | 91.0
Local Memory(SNC1) | 89.7 | 105.2 | 86.5 | 103.0
Remote Memory(SNC1) | 146.0 | 194.6 | 153.8 | 185.0
Cache Latency | ns (measured) |  | Cycles (calculated by Op-Freq) |  | Cycles (Ref: Fastest Load-to-use) | 
Cache Latency | ICX1519 | SPR97263 | ICX1519 | SPR97263 | ICX | SPR
L1 | 1.4 | 1.5 | 5.1 | 5.1 | 5 | 5
L2 | 4.9 | 5.4 | 17.8 | 18.4 | 14 | 16
Chart: L1/L2 Latency (cycle)
| L1 | L2
ICX1519 | 5.0904 | 17.8164
SPR97263 | 5.1045 | 18.3762
Chart: Latency(ns)
| L3(SNC4) | L3(SNC1) | Local Memory(SNC1) | Local Memory(SNC4) | Remote Memory(SNC1)
ICX1519 | 0 | 25.4 | 0 | 89.7 | 146
SPR97263 | 26 | 38 | 91.3 | 105.2 | 194.6
Ref : 20ww52.2_ICX_DDR_PnP_REPORT.pptx
https://sharepoint.amr.ith.intel.com/sites/server/ goto/SPR Architecture
EGS_Platform_Validation_Integration_Wave2_PnP_Update_WW17.pdf

## Slide 11: Bandwidth Comparison
11
11
Bandwidth measurement -- All cores generate threads to measure bandwidth. Specify read to write ratio for bandwidth thread.
cmd : ./mlc --loaded_latency -d0 -T -X -K1 -W3 (3R1W)
b/w (MB/s) | ICX(2s-76c76t) | HCC 24C | SPR(2s-120c120t) | Target
 | Meas | Ref: HCC 24cTarget | Meas | Ref: Target
100R | 322,145.5 | 348,600.0 | 533,692.2 | 540,910.0
3R1W | 284,495.1 | 289,000.0 | 469,356.3 | 477,450.0
1R1W | 262,793.9 | 249,600.0 | 439,137.4 | 462,640.0
DDR Max | 375,424.0 |  | 614,400.0 | 
b/w 100R > 3R1W >1R1W, more writing cause lower bandwidth
≈ = 0.611
Chart: b/w(MB/s)
| 100R | 3R1W | 1R1W
ICX-76c76t | 322145.5 | 284495.1 | 262793.9
SPR-120c120t | 533692.2 | 469356.3 | 439137.4
Ref : ICX from 20ww52.2_ICX_DDR_PnP_REPORT.pptx
SPR from https://sharepoint.amr.ith.intel.com/sites/server/ goto/SPR Architecture
EGS_Platform_Validation_Integration_Wave2_PnP_Update_WW17.pdf

## Slide 12: Bandwidth Comparison
12
12
Hyper-thread ON
cmd : ./mlc --loaded_latency -d0 -T -k0-37,76-113 (0-37,76-113 core works)
ICX(2s) b/w | run1 | run2 | run3 | run4 | run5 | Median | Theo (DDR4 Max b/w) | Median/Theo
0-37 | 163,309.7 | 163,388.8 | 163,292.8 | 161,308.4 | 163,026.5 | 163,292.8 | 187,712.0 | 90.0%
0-37,76-113 | 160,616.4 | 160,603.3 | 160,612.5 | 157,661.5 | 160,275.8 | 160,603.3 | 187,712.0 | 85.6%
0-75 | 325,754.3 | 325,727.0 | 325,418.3 | 325,790.4 | 324,538.2 | 325,727.0 | 375,424.0 | 86.8%
0-151(all cores) | 320,402.0 | 318,991.1 | 317,777.7 | 320,368.5 | 318,732.5 | 318,991.1 | 375,424.0 | 85.0%
SPR(2s) b/w | run1 | run2 | run3 | run4 | run5 | Median | Theo (DDR5 Max b/w) | Median/Theo
0-59 | 269,492.8 | 269,986.0 | 269,814.3 | 270,175.3 | 270,103.4 | 269,492.8 | 307,200.0 | 87.7%
0-59,120-179 | 263,191.6 | 263,246.7 | 262,809.9 | 262,802.2 | 263,147.1 | 263,147.1 | 307,200.0 | 85.6%
0-119 | 538,877.0 | 538,104.8 | 538,675.4 | 538,577.8 | 539,186.1 | 538,675.4 | 614,400.0 | 87.7%
0-239 (all cores) | 527,579.8 | 527,157.7 | 527,538.5 | 527,239.2 | 527,065.3 | 527,239.2 | 614,400.0 | 85.8%
Bandwidth of 2t/c is ~ 98% of bandwidth 1t/c

## Slide 13: Core Scaling Comparison – ICX(2s) vs SPR(2s)
13
13
Core Num | SPR97263 b/w (MB/s) | SPR97263 per core (MB/s) | ICX1519 b/w (MB/s) | ICX1519 per core (MB/s) | 
8 | 70,876.50 | 8,859.56 | 63,886.10 | 7,985.76 | 0.901
16 | 130,843.40 | 8,177.71 | 123,491.50 | 7,718.22 | 0.944
24 | 191,496.00 | 7,979.00 | 168,282.40 | 7,011.77 | 0.879
32 | 247,322.90 | 7,728.84 | 206,172.30 | 6,442.88 | 0.834
40 | 299,189.10 | 7,479.73 | 240,462.70 | 6,011.57 | 0.804
48 | 347,152.80 | 7,232.35 | 269,708.20 | 5,618.92 | 0.777
56 | 389,936.40 | 6,963.15 | 289,642.30 | 5,172.18 | 0.743
64 | 427,008.60 | 6,672.01 | 297,858.90 | 4,654.05 | 0.698
72 | 458,868.70 | 6,373.18 | 299,741.40 | 4,163.08 | 0.653
80 | 485,601.90 | 6,070.02 | 304,487.50 | 3,806.09 | 0.627
96 | 522,520.80 | 5,442.93 | 309,777.50 | 3,226.85 | 0.593
104 | 532,089.10 | 5,116.24 | 313,202.90 | 3,011.57 | 0.589
112 | 536,139.90 | 4,786.96 | 315,630.70 | 2,818.13 | 0.589
120 | 537,577.30 | 4,479.81 | 317,675.30 | 2,647.29 | 0.591
128 | 537,256.40 | 4,197.32 | 314,525.00 | 2,457.23 | 0.585
136 | 535,948.70 | 3,940.80 | 313,540.90 | 2,305.45 | 0.585
152 | 534,977.40 | 3,519.59 | 313,213.20 | 2,060.61 | 0.585
168 | 532,448.00 | 3,169.33 | / | / | /
184 | 531,052.60 | 2,886.16 | / | / | /
240 | 522,872.10 | 2,178.63 | / | / | /
Core Num | SPR97263 b/w (MB/s) | SPR97263 per core (MB/s) | ICX1519 b/w (MB/s) | ICX1519 per core (MB/s) | 
8 | 70,876.50 | 8,859.56 | 63,886.10 | 7,985.76 | 0.901
16 | 130,843.40 | 8,177.71 | 123,491.50 | 7,718.22 | 0.944
24 | 191,496.00 | 7,979.00 | 168,282.40 | 7,011.77 | 0.879
32 | 247,322.90 | 7,728.84 | 206,172.30 | 6,442.88 | 0.834
40 | 299,189.10 | 7,479.73 | 240,462.70 | 6,011.57 | 0.804
48 | 347,152.80 | 7,232.35 | 269,708.20 | 5,618.92 | 0.777
56 | 389,936.40 | 6,963.15 | 289,642.30 | 5,172.18 | 0.743
64 | 427,008.60 | 6,672.01 | 297,858.90 | 4,654.05 | 0.698
72 | 458,868.70 | 6,373.18 | 299,741.40 | 4,163.08 | 0.653
80 | 485,601.90 | 6,070.02 | 304,487.50 | 3,806.09 | 0.627
96 | 522,520.80 | 5,442.93 | 309,777.50 | 3,226.85 | 0.593
104 | 532,089.10 | 5,116.24 | 313,202.90 | 3,011.57 | 0.589
112 | 536,139.90 | 4,786.96 | 315,630.70 | 2,818.13 | 0.589
120 | 537,577.30 | 4,479.81 | 317,675.30 | 2,647.29 | 0.591
128 | 537,256.40 | 4,197.32 | 314,525.00 | 2,457.23 | 0.585
136 | 535,948.70 | 3,940.80 | 313,540.90 | 2,305.45 | 0.585
152 | 534,977.40 | 3,519.59 | 313,213.20 | 2,060.61 | 0.585
168 | 532,448.00 | 3,169.33 | / | / | /
184 | 531,052.60 | 2,886.16 | / | / | /
240 | 522,872.10 | 2,178.63 | / | / | /
The ratio of ICX/SPR bandwidth becomes as a stable value with the increase of working core number.
≈ = = = 0.611
Hyper-thread ON, cores are selected evenly in sockets and hyperthreading
cmd : ./mlc --loaded_latency -d0 -T -k0-3,60-63,120-123,180-183 (SPR 16core)

## Slide 14: SPR Core Scaling Comparison – QUAD(2s) vs SNC4(2s)
14
14
Hyper-thread ON, cores are selected evenly in sockets and hyperthreading
cmd : ./mlc --loaded_latency -d0 -T -k0-1,15-16,30-31,45-46,60-61,75-76,90-91,105-106 (SPR 16core)
Core Num | QUAD b/w (MB/s) | SNC4 b/w (MB/s) | SNC4/QUAD
8 | 129,348.50 | 143,793.50 | 1.112
16 | 238,191.60 | 257,890.60 | 1.083
24 | 322,038.50 | 329,572.20 | 1.023
32 | 333,227.40 | 331,421.70 | 0.995
40 | 427,445.20 | 431,177.50 | 1.009
48 | 485,959.60 | 510,517.10 | 1.051
56 | 539,536.60 | 551,555.10 | 1.022
64 | 546,923.60 | 555,987.70 | 1.017
72 | 545,551.10 | 554,561.10 | 1.017
80 | 544,026.00 | 552,365.40 | 1.015
96 | 542,060.20 | 548,847.40 | 1.013
104 | 541,129.20 | 548,537.40 | 1.014
112 | 539,505.60 | 547,208.50 | 1.014
120 | 535,711.70 | 546,422.30 | 1.020
128 | 535,293.50 | 546,750.10 | 1.021
136 | 534,460.10 | 545,798.60 | 1.021
152 | 533,922.80 | 543,537.20 | 1.018
168 | 531,934.00 | 541,669.30 | 1.018
184 | 531,250.50 | 541,388.50 | 1.019
240 | 510,185.60 | 537,428.30 | 1.053
SNC4 performance is a little better than QUAD.
Chart: SPR-QUAD vs SPR-SNC4
| 8 | 16 | 24 | 32 | 40 | 48 | 56 | 64 | 72 | 80 | 96 | 104 | 112 | 120 | 128 | 136 | 152 | 168 | 184 | 240
SPR-SNC4 | 143793.5 | 257890.6 | 329572.2 | 331421.7 | 431177.5 | 510517.1 | 551555.1 | 555987.7 | 554561.1 | 552365.4 | 548847.4 | 548537.4 | 547208.5 | 546422.3 | 546750.1 | 545798.6 | 543537.2 | 541669.3 | 541388.5 | 537428.3
SPR-QUAD | 129348.5 | 238191.6 | 322038.5 | 333227.4 | 427445.2 | 485959.6 | 539536.6 | 546923.6 | 545551.1 | 544026 | 542060.2 | 541129.2 | 539505.6 | 535711.7 | 535293.5 | 534460.1 | 533922.8 | 531934 | 531250.5 | 510185.6
DDR5 b/w (MB/s) | 614,400.00

## Slide 15
Conclusion.
  Same bandwidth test case on ICX and SPR, SPR performance is better than ICX.
  Both on ICX and SPR, with the increase of CPU core number, the performance would also increase at the beginning. Then it becomes stable.
  The ratio of ICX/SPR bandwidth is asymptotic the value of DDR speed ratio .
  With the same working cores, the SNC4 performance is a little better than QUAD.
Next Step:
  Try MLC’s more paraments for more features
  Try to help tuning other WL performance with MLC test case
15
Conclusion & Next Step

## Slide 16: Thank You
16