## Slide 1: WiE SF TSC WL Performance Stream –Micro Benchmark
Zhonghua,Sun
xPSD – Workload Integration and Enabling (WiE) team​
June.10.2022

## Slide 2: Content
Stream WSF Introduction
Perf Analysis
Gen-to-Gen Analysis
Scaling Threads
Bandwidth varies by diff core-location
Next Steps
2

## Slide 3: Introduction & Scope
The Stream workload is benchmark for system
sustainable bandwidth.
Data operation:
Memory->LLC->core(include L1/L2)->LLC->Memory.
Deploy Stream in Container for flexible simple usage.
WSF saturates CPU, Memory bandwidth, and
uncore resource amid accessing memory.
3
Performance Work Scope:
Bare Metal: ICX/SPR
Gen-to-Gen Comparison
Scaling threads
Bandwidth varies by diff core-location
Core
CHA
LLC
iMC
DRAM
DataRd
LookUp
Miss
MemRd(AD)
MRd
IDI_Data(BL)
MemData(AK/BL)
IDI_GO_E(AK)
Internal msg
Data

## Slide 4: Introduction
for (k=0; k<NTIMES; k++)
{ Copy
Scale
Add
Triad
}
http://www.cs.virginia.edu/stream/
www.cs.virginia.edu/stream/FTP/Code/stream.c
prepare…
#pragma omp parallel for
for (j=0; j<STREAM_ARRAY_SIZE; j++)
c[j] = = b[j]+scalar*a[j];
#endif
…
Get Min_Time from Time[k]
Time
KPI:
Triad
4
CPUs
LLC
Mem
CPUs
LLC
Mem
CPUs
LLC
Mem
CPUs
LLC
Mem
X
X
Triad
Scale
Copy
Add
STREAM_ARRAY_SIZE=
l3_cache_size * Num_sockets * 3.8 ( e.g., SPR, 896,532,480)
Array Type: 8 bytes

## Slide 5: Threading Model
5
#pragma omp parallel for
for (j=0; j<STREAM_ARRAY_SIZE; j++)
c[j] = = b[j]+scalar*a[j];
#endif
Multiple threads execute the operation together.
Number of threads:
OMP_NUM_THREADS=Num_Socket*
Cores_Per_Socket*
Thread_Per_Core
UPI
DDR
Thread, Thread… Thread, Thread …
KMP_AFFINITY=Compact,1
Socket_1
Socket_0
DDR
UPI
Socket_1
Socket_0
DDR
Core scaling mode 2 for SPR
Same logical core number in all dies
DDR
Core scaling mode 1 for ICX/SPR
Same logical core number in both socket
Notes: KMP_AFFINITY=Scatter

## Slide 6: Flow and Impactions
Test architecture and principle
6
Compile Stream.c
Run Stream
Output Result
Condition | Target | Setting | Comments
Compiler | ICC for IA Affinity parameters | ICC (2021.3.0.3168) | Choose parameters
STREM_ARRY_SIZE | Size enough to cover LLC | 4 x LLC*Socket | Tune
NTIMES | looping number to keep stable result | Default:e.g, 100 | NTIMES >= 2
Multiple threads | Saturate all CPUs | number of CPUs | Best to make: 1 CPU 1 Thread
To confirm full memory operation with minimum cost of time:
Build Stream

## Slide 7: Case and KPI
4 basic cases
7
Function Best Rate (MB/s) Avg time (s) Min time (s) Max time (s)
Triad: 407,599.9 0.147309 0.052789 0.213000
icc -O3 -parallel –qopenmp-link static -x${arch} -qopenmp -mcmodel=medium -DSTREAM_ARRAY_SIZE=${array_size} -DNTIMES=${NTIMES} stream.c -o stream -ffreestanding
Arch | comments
Default | SSE
CORE-AVX2 | Support Intel AVX2, compatilbe with SSE*
COMMON-AVX512 | Support Intel AVX-512 and compatible with AVX2
SSE | SSE4.2, generate Intel SSE4 Instructions
Case result, Sample:

## Slide 8: Software Stack
Orchestration/ containers
Host OS
CentOS/Ubuntu
K8S
Workloads
Intel SPR/ICX
hardware
Stream
WSF
Component | Version
Compiler ICC | 2021.3.0.3168
Stream | Revision 5.10 www.cs.virginia.edu/stream/FTP/Code/stream.c
Container OS | Rocky Linux 8.5
Host OS/Kernel | SPR(5.15.0-spr.bkc.pc.2.10.0.x86_64) ICX(4.18.0-305.19.1.el8_4.x86_64）
Host | SPR/ICX
8

## Slide 9: BareMetal Configuration(SPR/ICX)
Manufacturer | Intel Corporation | Intel Corporation
Product Name | ArcherCity-SPR | WilsonCity-ICX
BIOS Version | EGSDCRB1.86B.0073.D14.2201260628 | WLYDCRB1.SYS.0027.P56.2112200409
OS | CentOS Stream 8 | Red Hat Enterprise Linux 8.2 (Ootpa)
Kernel | 5.15.0-spr.bkc.pc.2.10.0.x86_64 | 4.18.0-305.19.1.el8_4.x86_64
Microcode | 0x8e0001c0 | 0xd000332
IRQ Balance | Enabled | Enabled
CPU Model | Genuine Intel(R) CPU-Q03J | Intel(R) Xeon(R) Platinum 8368Q CPU @ 2.60GHz
Base Frequency | 1.6GHz | 2.6GHz
Maximum Frequency | 3.5GHz | 3.7GHz
All-core Maximum Frequency | 2.6GHz | 3.3GHz
CPU(s) | 240 | 152
Base Frequency(AVX2) | NA | 2.3GHz
Maximum Frequency(AVX2) | 3.5GHz | 3.6GHz
All-core Maximum Frequency(AVX2) | 2.5GHz | 3.2GHz
Base Frequency(AVX3) | NA | 1.9GHz
Maximum Frequency(AVX3) | 3.5GHz | 3.5GHz
All-core Maximum Frequency(AVX3) | 2.3GHz | 2.6GHz
Thread(s) per Core | 2 | 2
Core(s) per Socket | 60 | 76
Socket(s) | 2 | 2
NUMA Node(s) | 2 | 2
L3 Cache | 115200K | 58368K
Prefetchers | DCU HW, DCU IP, L2 HW, L2 Adj | DCU HW, DCU IP, L2 HW, L2 Adj.
Turbo | Enabled | Enabled
PPIN(s) | 5df94908a5e86db4, 5df949ed3b1ebf7f | 57ff4edc2432918d, 4b1245dcd2110525
Power & Perf Policy | Performance | Performance
TDP | 350 watts | 270 watts
Frequency Driver | Intel_pstate | Intel_pstate
Frequency Governer | performance | performance
Frequency (MHz) | 2600 | 2767
Max C-State | 9 | 9
Installed Memory | 512GB (16x32GB 4800MT/s [4800MT/s]) | 512GB (16x32GB DDR4 2933MT/s [2933MT/s])
Huge Pages Size | 2048 kB | 2048 kB
Transparent Huge Pages | always | always
Automatic NUMA Balancing | Enabled | Enabled
9

## Slide 10: Gen-to-Gen AVX3-Case Triad result
 | Metric | Run1 | Run2 | Run3 | Run4 | Run5 | Median | Standard Deviation | Average
Max Bandwidth | MB/s | 462,755.2 | 466,812.4 | 465,308.2 | 465,670.7 | 465,872.6 | 465,670.1 | 1518.83 | 465,283.82
CPU utilization | % | 98.11 | 97.76 | 97.88 | 97.78 | 98.11 | / | / | /
CPU Freq | GHz | 2.59 | 2.59 | 2.59 | 2.59 | 2.59 | / | / | /
SPR 240 cores
 | Metric | Run1 | Run2 | Run3 | Run4 | Run5 | Median | Standard Deviation | Average
Max Bandwidth | MB/s | 279,305.2 | 279,283 | 278,690.6 | 278,734.8 | 279,155.1 | 279,155.1 | 299.02 | 279,033.74
CPU utilization | % | 99.8 | 99.81 | 100 | 99.89 | 99.7 | / | / | /
CPU Freq | GHz | 2.96 | 2.87 | 2.84 | 2.94 | 2.94 | / | / | /
ICX 152 cores
10

## Slide 11: Emon: SPR-240 cores/ICX-152 cores
 | SPR-socket 0 | SPR-socket 1 | ICX-socket 0 | ICX-socket 1
metric_CPU operating frequency (in GHz) | 2.5906 | 2.5898 | 2.9518 | 2.9276
metric_CPU utilization % | 97.8903 | 97.8682 | 99.6963 | 99.7136
metric_CPI | 14.6368 | 13.8203 | 17.2435 | 17.0722
metric_DDR data rate (MT/sec) | 4,803.3076 | 4,803.0420 | 2,935.1312 | 2,935.5737
metric_memory bandwidth read (MB/sec) | 134,273.4726 | 133,120.0976 | 80,185.7381 | 80,348.5731
metric_memory bandwidth write (MB/sec) | 86,387.0547 | 86,380.1466 | 53,527.9849 | 53,563.7229
metric_memory bandwidth total (MB/sec) | 220,660.5272 | 219,500.2442 | 133,713.7231 | 133,912.2960
metric_uncore frequency GHz | 2.1058 | 2.1313 | 2.0728 | 1.9900
metric_TMA_Frontend_Bound(%) | 2.2621 | 2.3533 | 2.3091 | 1.7621
metric_TMA_Bad_Speculation(%) | 0.1353 | 0.1401 | 0.2165 | 0.2158
metric_TMA_Retiring(%) | 2.7408 | 2.9288 | 2.4984 | 2.5180
metric_TMA_Backend_Bound(%) | 94.8618 | 94.5778 | 94.9759 | 95.5041
metric_TMA_..Memory_Bound(%) | 90.6180 | 90.0453 | 92.1807 | 92.6654
metric_TMA_....L1_Bound(%) | 2.4280 | 1.1349 | 6.7498 | 6.4098
metric_TMA_......DTLB_Load(%) | 0.0437 | 0.0399 | 0.0431 | 0.0478
metric_TMA_......Split_Loads(%) | 0.0023 | 0.0021 | 0.0003 | 0.0001
metric_TMA_......4K_Aliasing(%) | 0.0001 | 0.0001 | 0.0037 | 0.0043
metric_TMA_......FB_Full(%) | 74.7694 | 73.9631 | 78.3159 | 78.4800
metric_TMA_....L2_Bound(%) | 0.3229 | 0.2935 | 0.5682 | 0.6051
metric_TMA_....L3_Bound(%) | 11.0865 | 9.4865 | 3.6914 | 3.9014
metric_TMA_......Data_Sharing(%) | 0.0059 | 0.0075 | 0.0034 | 0.0040
metric_TMA_......L3_Hit_Latency(%) | 0.0663 | 0.0612 | 0.1940 | 0.1730
metric_TMA_......SQ_Full(%) | 43.6097 | 43.9935 | 29.9709 | 30.8629
metric_TMA_....DRAM_Bound(%) | 76.4144 | 78.9253 | 85.1820 | 85.0731
metric_TMA_......MEM_Bandwidth(%) | 91.0163 | 90.8085 | 76.6569 | 76.6683
metric_TMA_......MEM_Latency(%) | 4.1628 | 4.4404 | 14.4305 | 14.9356
metric_TMA_........Local_DRAM(%) | 42.3132 | 44.1384 | 27.6470 | 27.5714
metric_TMA_........Remote_DRAM(%) | 0.0846 | 0.0832 | 0.0920 | 0.0740
metric_TMA_........Remote_Cache(%) | 0.0088 | 0.0090 | 0.0083 | 0.0075
metric_TMA_....Store_Bound(%) | 0.0297 | 0.0351 | 0.0533 | 0.0617
metric_TMA_..Core_Bound(%) | 4.2439 | 4.5325 | 2.7952 | 2.8387
11

## Slide 12: Gen-to-Gen core Scaling
Chart: System bandwidth SPR vs ICX
| 4 | 8 | 16 | 24 | 32 | 40 | 48 | 56 | 64 | 72 | 80 | 88 | 96 | 104 | 112 | 120 | 128 | 136 | 152 | 168 | 180 | 196 | 240
SPR-Triad | 74843.3 | 142470.7 | 262000.5 | 354349.7 | 415414.2 | 450642.5 | 464685.2 | 472178.3 | 447278.9 | 456956.1 | 464443.7 | 469654.7 | 470445.5 | 471310.3 | 470774.4 | 470570.6 | 424109.3 | 440132.8 | 460420.4 | 467104.8 | 466773.8 | 464826.4 | 463403.9
ICX-Triad | 75225 | 138060.8 | 225738.6 | 256604.3 | 271054.9 | 278570.1 | 280830.2 | 280403.1 | 279956.7 | 278505.6 | 248140.6 | 262846.8 | 262846.8 | 272416.2 | 272941.5 | 273052.3 | 272655 | 272226.5 | 270564.1
SPR-ICX Ratio | 0.99493 | 1.0319 | 1.1606 | 1.3809 | 1.5326 | 1.6177 | 1.6547 | 1.6839 | 1.5977 | 1.6407 | 1.8717 | 1.7868 | 1.7898 | 1.7301 | 1.7248 | 1.7234 | 1.5555 | 1.6168 | 1.7017
Core number | SPR | ICX | SPR per core | ICX per core
 | BW MB/s |  |  | 
4 | 74,843.3 | 75,225 | 18,711 | 18,806
8 | 142,470.7 | 138,060.8 | 17,809 | 17,258
16 | 262,000.5 | 225,738.6 | 16,375 | 14,109
24 | 354,349.7 | 256,604.3 | 14,765 | 10,692
32 | 415,414.2 | 271,054.9 | 12,982 | 8,470
40 | 450,642.5 | 278,570.1 | 11,266 | 6,964
48 | 464,685.2 | 280,830.2 | 9,681 | 5,851
56 | 472,178.3 | 280,403.1 | 8,432 | 5,007
64 | 447,278.9 | 279,956.7 | 6,989 | 4,374
72 | 456,956.1 | 278,505.6 | 6,347 | 3,868
80 | 464,443.7 | 248,140.6 | 5,806 | 3,102
88 | 469,654.7 | 262,846.8 | 5,337 | 2,987
96 | 470,445.5 | 262,846.8 | 4,900 | 2,738
104 | 471,310.3 | 272,416.2 | 4,532 | 2,619
112 | 470,774.4 | 272,941.5 | 4,203 | 2,437
120 | 470,570.6 | 273,052.3 | 3,921 | 2,275
128 | 424,109.3 | 272,655 | 3,313 | 2,130
136 | 440,132.8 | 272,226.5 | 3,236 | 2,002
152 | 460,420.4 | 270,564.1 | 3,029 | 1,780
168 | 467,104.8 |  | 2,780 | 
180 | 466,773.8 |  | 2,593 | 
196 | 464,826.4 |  | 2,372 | 
240 | 463,403.9 |  | 1,931 | 
= =
Chart: Per core bandwidth SPR vs ICX
| 4 | 8 | 16 | 24 | 32 | 40 | 48 | 56 | 64 | 72 | 80 | 88 | 96 | 104 | 112 | 120 | 128 | 136 | 152 | 168 | 180 | 196 | 240
SPR per-core | 18710.825 | 17808.8375 | 16375.0312 | 14764.5708 | 12981.6938 | 11266.0625 | 9680.9417 | 8431.7554 | 6988.7328 | 6346.6125 | 5805.5463 | 5336.9852 | 4900.474 | 4531.8298 | 4203.3429 | 3921.4217 | 3313.3539 | 3236.2706 | 3029.0816 | 2780.3857 | 2593.1878 | 2371.5633 | 1930.8496
ICX per-core | 18806.25 | 17257.6 | 14108.6625 | 10691.8458 | 8470.4656 | 6964.2525 | 5850.6292 | 5007.1982 | 4374.3234 | 3868.1333 | 3101.7575 | 2986.8955 | 2737.9875 | 2619.3865 | 2436.9777 | 2275.4358 | 2130.1172 | 2001.6654 | 1780.027
12

## Slide 13: SPR core Scaling: mode 1 vs mode 2
core number | Scatter by Die (SNC4-Enabled) | Scatter by socket (2NUMA-Enabled)
 | BW MB/s | BW MB/s
4 | / | 74,843.3
8 | 145,376.9 | 142,470.7
16 | 257,651.7 | 262,000.5
24 | 342,744.0 | 354,349.7
32 | 394,745.6 | 415,414.2
40 | 425,601.3 | 450,642.5
48 | 450,489.5 | 464,685.2
56 | 464,522.6 | 472,178.3
64 | 470,764.5 | 447,278.9
72 | 472,356.3 | 456,956.1
80 | 472,781.9 | 464,443.7
88 | / | 469,654.7
96 | 475,214.1 | 470,445.5
104 | / | 471,310.3
112 | 478,715.4 | 470,774.4
120 | 468,163.7 | 470,570.6
128 | 449,484.3 | 424,109.3
136 | 460,023.7 | 440,132.8
152 | 459,829.2 | 460,420.4
168 | 474,073.3 | 467,104.8
180 | / | 466,773.8
184 | 476,192.0 | /
196 | / | 464,826.4
240 | 475,529.6 | 463,403.9
Chart: Scattering working cores by sockets/dies
| 4 | 8 | 16 | 24 | 32 | 40 | 48 | 56 | 64 | 72 | 80 | 88 | 96 | 104 | 112 | 120 | 128 | 136 | 152 | 168 | 180 | 184 | 196 | 240
scatter-8Die | 145376.9 | 257651.7 | 342744 | 394745.6 | 425601.3 | 450489.5 | 464522.6 | 470764.5 | 472356.3 | 472781.9 | 475214.1 | 478715.4 | 468163.7 | 449484.3 | 460023.7 | 459829.2 | 474073.3 | 476192 | 475529.6
scatter-2socket | 74843.3 | 142470.7 | 262000.5 | 354349.7 | 415414.2 | 450642.5 | 464685.2 | 472178.3 | 447278.9 | 456956.1 | 464443.7 | 469654.7 | 470445.5 | 471310.3 | 470774.4 | 470570.6 | 424109.3 | 440132.8 | 460420.4 | 467104.8 | 466773.8 | 464826.4 | 463403.9
After bandwidth reaching roofline,
scattering threads by Dies, deliver
higher bandwidth.
13
Notes: BM SF Emon:
x264link
x265 link:
BM FMB emon:
AWS-22.13: https://cumulus-dashboard.intel.com/services-framework/run_uri/5ecd8dd7d5e1-9a9ece31-ef19-4664-ace1-a68bd38219ca
AWS-22.13:

## Slide 14: Bandwidth varies by diff Core-Location
14
0 | 1 | 2 | 3 |  | 33 | 32 | 31 | 30
MC | 4 | 5 | 6 |  | 36 | 35 | 34 | MC
7 | 8 | 9 | 10 |  | 40 | 39 | 38 | 37
11 | 12 | 13 | 14 |  | 44 | 43 | 42 | 41
26 | 27 | 28 | 29 |  | 59 | 58 | 57 | 56
22 | 23 | 24 | 25 |  | 55 | 54 | 53 | 52
MC | 19 | 20 | 21 |  | 51 | 50 | 49 | MC
15 | 16 | 17 | 18 |  | 48 | 47 | 46 | 45
60 | 61 | 62 | 63 |  | 93 | 92 | 91 | 90
MC | 64 | 65 | 66 |  | 96 | 95 | 94 | MC
67 | 68 | 69 | 70 |  | 100 | 99 | 98 | 97
71 | 72 | 73 | 74 |  | 104 | 103 | 102 | 101
86 | 87 | 88 | 89 |  | 119 | 118 | 117 | 116
82 | 83 | 84 | 85 |  | 115 | 114 | 113 | 112
MC | 79 | 80 | 81 |  | 111 | 110 | 109 | MC
75 | 76 | 77 | 78 |  | 108 | 107 | 106 | 105
Case | Metric | Run1 | Run2 | Run3 | Run4 | Run5 | Average
copy | MB/s | 159,014.3 | 159,394.3 | 159220.9 | 159,220.9 | 158,811.5 | 159,132.38
scale | MB/s | 158,637.8 | 158,657.4 | 158522.4 | 158,522.4 | 158,375.1 | 158,543.02
Add | MB/s | 145,094 | 145,037.6 | 144,893 | 144,893 | 144,839.5 | 144,951.48
Triad | MB/s | 144,856 | 144,502.1 | 144732.4 | 144,732.4 | 144,608.8 | 144,686.34
Case | Metric | Run1 | Run2 | Run3 | Run4 | Run5 | Average
copy | MB/s | 162,959.9 | 163,000.5 | 162,822.7 | 162,990.8 | 162,911.3 | 162,937.04
scale | MB/s | 162,652.8 | 162,542.5 | 162,599.2 | 162,658.1 | 162,693.3 | 162,629.18
Add | MB/s | 149,222.9 | 149,280.2 | 149,077.5 | 149,286.3 | 149,108.5 | 149,195.08
Triad | MB/s | 149,008.3 | 149,073.0 | 148,914.4 | 149,124.0 | 148,908.2 | 149,005.58
Case | Metric | Run1 | Run2 | Run3 | Run4 | Run5 | Average
copy | MB/s | 163,473.9 | 163,323.5 | 163,591.7 | 163,494.4 | 163,567.3 | 163,490.16
scale | MB/s | 163,126.5 | 162,994.8 | 163,273 | 163,095.1 | 163,277 | 163,153.28
Add | MB/s | 149,957.3 | 149,816.4 | 149,975 | 149,958.6 | 149,964.8 | 149,934.42
Triad | MB/s | 149,787.3 | 149,643.3 | 149,816.4 | 149,790.3 | 149,826.9 | 149,772.84
Case | Metric | Run1 | Run2 | Run3 | Run4 | Run5 | Average
copy | MB/s | 162,134.3 | 162,115.9 | 162,136.0 | 162,163.6 | 162,039.1 | 162,117.78
scale | MB/s | 161,690.3 | 161,688.5 | 161,721.1 | 161,806.8 | 161,752.4 | 161,731.82
Add | MB/s | 148,512.5 | 148,454.1 | 148,473.6 | 148,497.1 | 148,406.7 | 148,468.80
Triad | MB/s | 148,300.4 | 148,246.6 | 148,302.6 | 148,327.9 | 148,160.7 | 148,267.64
Chart: Normalized data for 4 group of cores
| Set 1 | Set 4 | Set 2 | Set 3
 | 1 | 1.0247 | 1.0295 | 1.0349
Set 1 CORE: 0,15,30,45,60,75,90,105
Set 2 CORE: 1,16,31,46,61,76,91,106
Set 3 CORE: 4,19,34,49,64,79,94,109
Set 4 CORE: 14,29,44,59,74,89,104,119

## Slide 15
Chart: SPR_TMA_Backend_Bound(%)
| 8cores-Skt0 | 8cores-Skt1 | 16cores-Skt0 | 16cores-Skt1 | 24cores-Skt0 | 24cores-Skt1 | 32cores-Skt0 | 32cores-Skt1 | 40cores-Skt0 | 40cores-Skt1 | 48cores-Skt0 | 48cores-Skt1 | 56cores-Skt0 | 56cores-Skt1 | 64cores-Skt0 | 64cores-Skt1 | 72cores-Skt0 | 72cores-Skt1 | 80cores-Skt0 | 80cores-Skt1 | 88cores-Skt0 | 88cores-Skt1 | 96cores-Skt0 | 96cores-Skt1 | 104cores-Skt0 | 104cores-Skt1 | 112cores-Skt0 | 112cores-Skt1 | cores120-Skt0 | cores120-Skt1 | 128cores-Skt0 | 128cores-Skt1 | 136cores-Skt0 | 136cores-Skt1 | 152cores-Skt0 | 152cores-Skt1 | 168cores-Skt0 | 168cores-Skt1 | 240cores-Skt0 | 240cores-Skt1
metric_TMA_Backend_Bound(%) | 93.8076 | 93.7464 | 95.0141 | 94.665 | 95.5809 | 95.6985 | 96.1097 | 96.2116 | 96.5978 | 96.4381 | 97.0067 | 96.6595 | 97.115 | 96.8625 | 96.38 | 96.0493 | 96.6468 | 96.4865 | 97.0004 | 96.8808 | 97.2776 | 97.1666 | 97.5398 | 97.3886 | 97.7025 | 97.558 | 97.8564 | 97.6413 | 97.7604 | 97.6314 | 94.843 | 94.7326 | 94.8233 | 94.5217 | 94.3794 | 93.9765 | 93.932 | 93.4981 | 94.203 | 93.7093
Core scaling for SPR : memory bound analysis (Scaling mode 1)
Chart: SPR_TMA_..Memory_Bound(%)
| 8cores-Skt0 | 8cores-Skt1 | 16cores-Skt0 | 16cores-Skt1 | 24cores-Skt0 | 24cores-Skt1 | 32cores-Skt0 | 32cores-Skt1 | 40cores-Skt0 | 40cores-Skt1 | 48cores-Skt0 | 48cores-Skt1 | 56cores-Skt0 | 56cores-Skt1 | 64cores-Skt0 | 64cores-Skt1 | 72cores-Skt0 | 72cores-Skt1 | 80cores-Skt0 | 80cores-Skt1 | 88cores-Skt0 | 88cores-Skt1 | 96cores-Skt0 | 96cores-Skt1 | 104cores-Skt0 | 104cores-Skt1 | 112cores-Skt0 | 112cores-Skt1 | cores120-Skt0 | cores120-Skt1 | 128cores-Skt0 | 128cores-Skt1 | 136cores-Skt0 | 136cores-Skt1 | 152cores-Skt0 | 152cores-Skt1 | 168cores-Skt0 | 168cores-Skt1 | 240cores-Skt0 | 240cores-Skt1
metric_TMA_..Memory_Bound(%) | 85.0329 | 84.8405 | 87.0444 | 86.3475 | 88.433 | 88.32 | 89.8497 | 89.6562 | 90.6158 | 90.0725 | 91.7017 | 90.4141 | 92.337 | 90.6679 | 88.039 | 86.0281 | 88.9518 | 87.8812 | 90.3787 | 89.4001 | 91.3154 | 90.7567 | 92.4525 | 91.4766 | 93.0577 | 92.1637 | 93.6754 | 92.4118 | 93.2087 | 92.3677 | 79.7006 | 78.6357 | 79.9878 | 78.5517 | 78.7602 | 77.4547 | 78.0104 | 76.5082 | 89.4422 | 88.6367
15

## Slide 16: Core scaling for ICX : memory bound analysis (Scaling mode 1)
Chart: ICX_TMA_Backend_Bound(%)
| 4C-Skt0 | 4C-Skt1 | 8C-Skt0 | 8C-Skt1 | 16C-Skt0 | 16C-Skt1 | 24C-Skt0 | 24C-Skt1 | 32C-Skt0 | 32C-Skt1 | 40C-Skt0 | 40C-Skt1 | 48C-Skt0 | 48C-Skt1 | 56C-Skt0 | 56C-Skt1 | 64C-Skt0 | 64C-Skt1 | 72C-Skt0 | 72C-Skt1 | 80C-Skt0 | 80C-Skt1 | 88C-Skt0 | 88C-Skt1 | 96C-Skt0 | 96C-Skt1 | 104C-Skt0 | 104C-Skt1 | 112C-Skt0 | 112C-Skt1 | 120C-Skt0 | 120C-Skt1 | 128C-Skt0 | 128C-Skt1 | 136C-Skt0 | 136C-Skt1 | 152C-Skt0 | 152C-Skt1
metric_TMA_Backend_Bound(%) | 92.1898 | 92.7124 | 93.0518 | 92.9766 | 94.6961 | 94.6789 | 96.0311 | 95.9002 | 96.3188 | 96.4 | 94.5781 | 95.6792 | 95.6275 | 96.3957 | 97.0774 | 97.344 | 97.5635 | 97.7497 | 97.7536 | 97.9095 | 91.9012 | 92.9008 | 91.4748 | 92.0013 | 92.1136 | 91.6669 | 92.0125 | 91.878 | 92.0455 | 91.7076 | 92.5237 | 92.2361 | 93.0865 | 93.07 | 94.5467 | 94.24 | 95.1128 | 95.4014
Chart: ICX_TMA_..Memory_Bound(%)
| 4C-Skt0 | 4C-Skt1 | 8C-Skt0 | 8C-Skt1 | 16C-Skt0 | 16C-Skt1 | 24C-Skt0 | 24C-Skt1 | 32C-Skt0 | 32C-Skt1 | 40C-Skt0 | 40C-Skt1 | 48C-Skt0 | 48C-Skt1 | 56C-Skt0 | 56C-Skt1 | 64C-Skt0 | 64C-Skt1 | 72C-Skt0 | 72C-Skt1 | 80C-Skt0 | 80C-Skt1 | 88C-Skt0 | 88C-Skt1 | 96C-Skt0 | 96C-Skt1 | 104C-Skt0 | 104C-Skt1 | 112C-Skt0 | 112C-Skt1 | 120C-Skt0 | 120C-Skt1 | 128C-Skt0 | 128C-Skt1 | 136C-Skt0 | 136C-Skt1 | 152C-Skt0 | 152C-Skt1
metric_TMA_..Memory_Bound(%) | 81.4403 | 81.0366 | 80.5921 | 80.1682 | 85.1336 | 84.8911 | 89.2711 | 88.7791 | 90.3331 | 88.5264 | 85.5256 | 86.8704 | 89.199 | 89.9486 | 91.3806 | 92.1575 | 93.7812 | 94.4729 | 91.2382 | 91.1269 | 78.1679 | 80.1821 | 80.6268 | 79.3728 | 81.022 | 80.0564 | 82.2225 | 81.4853 | 80.719 | 79.9601 | 81.3173 | 80.9951 | 83.5801 | 83.218 | 88.345 | 87.6466 | 81.7997 | 81.9246
16

## Slide 17: Core scaling for SPR : memory bound analysis (Scaling mode 2)
Chart: SPR_TMA_Backend_Bound(%)
| 8C-Skt0 | 8C-Skt1 | 16C-Skt0 | 16C-Skt1 | 24C-Skt0 | 24C-Skt1 | 32C-Skt0 | 32C-Skt1 | 40C-Skt0 | 40C-Skt1 | 48C-Skt0 | 48C-Skt1 | 56C-Skt0 | 56C-Skt1 | 64C-Skt0 | 64C-Skt1 | 72C-Skt0 | 72C-Skt1 | 80C-Skt0 | 80C-Skt1 | 96C-Skt0 | 96C-Skt1 | 112C-Skt0 | 112C-Skt1 | 120C-Skt0 | 120C-Skt1 | 128C-Skt0 | 128C-Skt1 | 136C-Skt0 | 136C-Skt1 | 152C-Skt0 | 152C-Skt1 | 168C-Skt0 | 168C-Skt1 | 184C-Skt0 | 184C-Skt1 | 240C-Skt0 | 240C-Skt1
metric_TMA_Backend_Bound(%) | 93.6686 | 94.134 | 94.7158 | 94.866 | 95.5766 | 95.7271 | 96.3008 | 96.304 | 96.6664 | 96.6429 | 96.8478 | 96.8073 | 97.0453 | 96.8227 | 97.2012 | 97.1132 | 97.4471 | 97.346 | 97.6295 | 97.4322 | 97.7453 | 97.8076 | 97.8105 | 97.6204 | 97.7567 | 97.5851 | 95.5575 | 95.5254 | 95.3302 | 95.2429 | 94.461 | 94.2419 | 94.1497 | 93.8918 | 94.1427 | 93.9661 | 94.7787 | 94.4577
Chart: SPR_TMA_..Memory_Bound(%)
| 8C-Skt0 | 8C-Skt1 | 16C-Skt0 | 16C-Skt1 | 24C-Skt0 | 24C-Skt1 | 32C-Skt0 | 32C-Skt1 | 40C-Skt0 | 40C-Skt1 | 48C-Skt0 | 48C-Skt1 | 56C-Skt0 | 56C-Skt1 | 64C-Skt0 | 64C-Skt1 | 72C-Skt0 | 72C-Skt1 | 80C-Skt0 | 80C-Skt1 | 96C-Skt0 | 96C-Skt1 | 112C-Skt0 | 112C-Skt1 | 120C-Skt0 | 120C-Skt1 | 128C-Skt0 | 128C-Skt1 | 136C-Skt0 | 136C-Skt1 | 152C-Skt0 | 152C-Skt1 | 168C-Skt0 | 168C-Skt1 | 184C-Skt0 | 184C-Skt1 | 240C-Skt0 | 240C-Skt1
metric_TMA_..Memory_Bound(%) | 82.1559 | 82.6153 | 83.6381 | 83.5745 | 86.0441 | 86.2047 | 88.179 | 87.9351 | 89.073 | 88.6071 | 89.5939 | 89.086 | 90.2753 | 89.437 | 90.6055 | 90.0013 | 91.3938 | 90.6118 | 91.8755 | 90.9308 | 92.335 | 92.1947 | 92.3332 | 91.5466 | 92.1979 | 91.2726 | 82.2001 | 81.8215 | 81.6803 | 81.2726 | 78.8585 | 78.1152 | 78.9112 | 78.1284 | 80.033 | 79.531 | 90.4307 | 89.8296
17

## Slide 18: Conclusion & Next Steps
Conclusion:
Stream WL shows system memory bandwidth is mainly impacted by DDR bandwidth.
Scatter tasks on dies on average, better output for bandwidth.
Next step:
Tuning parameters, Select more parameters in IA affinity for Memory and bandwidth;
Design and implement more cases, e.g, TMUL, AMX
Investigate more scenarios, Pmem, HBM and other.
18

## Slide 19: Thank You
19